## Slide 1
User Input
Priority: ∞ Period: 50 ms Description: Monitors for user input to perform actions
Motor Controller
Priority: 2 Period: 20 ms Description: Sets motor speed and updates encoders (will include closed loop motor control)
Data Transfer
Priority: 1 Period: 20 ms Description: Transfers small amounts of data at a time
Garbage Collector
Priority: 0 Period: 0 ms Description: When no other tasks are running collect garbage data for defragmentation
l_flag_s:
[uint8]
r_flag_s:
[uint8]
l_speed_s:
[float]
r_speed_s:
[float]
l_time_q:
[uint32]
l_pos_q:
[float]
l_vel_q:
[float]
r_pos_q:
[float]
r_vel_q:
[float]
r_time_q:
[uint32]
data_transfer_s:
[uint8]
Path Director
Priority: 3 Period: 30 ms Description: A control algorithm that divides Romi’s actions into sequential segments, each defining distinct behavior and actions.
Observer
Priority: 2 Period: 20 ms Description: Discretized linear model of Romi’s state and input variables to best estimate the current position and orientation.
cal_white_s:
[uint8]
cal_black_s:
[uint8]
seg_start_s:
[uint8]
test_complete_s:
[uint8]
set_seg_s:
[uint8]
obsd_lpos_s:
[float]
obsd_rpos_s:
[float]
obsd_cpos_s:
[float]
obsd_yaw_s:
[float]
obsd_yawrate_s:
[float]
obsd_X_s:
[float]
obsd_Y_s:
[float]

## Slide 2
User Input
Priority: ∞ Period: 50 ms Description: Monitors for user input to perform actions
Motor Controller
Priority: 2 Period: 20 ms Description: Sets motor speed and updates encoders (will include closed loop motor control)
Data Transfer
Priority: 1 Period: 20 ms Description: Transfers small amounts of data at a time
Garbage Collector
Priority: 0 Period: 0 ms Description: When no other tasks are running collect garbage data for defragmentation
l_flag_s:
[uint8]
r_flag_s:
[uint8]
l_speed_s:
[float]
r_speed_s:
[float]
l_time_q:
[uint32]
l_pos_q:
[float]
l_vel_q:
[float]
r_pos_q:
[float]
r_vel_q:
[float]
r_time_q:
[uint32]
data_transfer_s:
[uint8]
test_complete_s:
[uint8]
Path Director
Priority: 3 Period: 30 ms Description: A control algorithm that divides Romi’s actions into sequential segments, each defining distinct behavior and actions.
Observer
Priority: 2 Period: 20 ms Description: Discretized linear model of Romi’s state and input variables to best estimate the current position and orientation.
obsd_lpos_s:
[float]
obsd_rpos_s:
[float]
obsd_yaw_s:
[float]
obsd_yawrate_s:
[float]
cal_white_s:
[uint8]
cal_black_s:
[uint8]
set_seg_s:
[uint8]
seg_start_s:
[uint8]

## Slide 3
User Input
Priority: ∞ Period: 50 ms Description: Monitors for user input to perform actions
Motor Controller
Priority: 2 Period: 20 ms Description: Sets motor speed and updates encoders (will include closed loop motor control)
Data Transfer
Priority: 1 Period: 20 ms Description: Transfers small amounts of data at a time
Garbage Collector
Priority: 0 Period: 0 ms Description: When no other tasks are running collect garbage data for defragmentation
l_flag_s:
[uint8]
r_flag_s:
[uint8]
l_speed_s:
[float]
r_speed_s:
[float]
l_time_q:
[uint32]
l_pos_q:
[float]
l_vel_q:
[float]
r_pos_q:
[float]
r_vel_q:
[float]
r_time_q:
[uint32]
data_transfer_s:
[uint8]
test_complete_s:
[uint8]
Path Director
Priority: 3 Period: 30 ms Description: A control algorithm that divides Romi’s actions into sequential segments, each defining distinct behavior and actions.
Observer
Priority: 2 Period: 20 ms Description: Discretized linear model of Romi’s state and input variables to best estimate the current position and orientation.
obsd_lpos_s:
[float]
obsd_rpos_s:
[float]
obsd_yaw_s:
[float]
obsd_yawrate_s:
[float]
cal_white_s:
[uint8]
cal_black_s:
[uint8]
set_seg_s:
[uint8]
seg_start_s:
[uint8]
l_flag_s:
[uint8]
r_flag_s:
[uint8]
l_speed_s:
[float]

## Slide 4
User Input Task
Check for Inputs from UART
Pop Cmd from Queue
T
F
Add Input to Cmd Queue
Single-Input Action
Perform Action
Check for n-number of inputs (action dependent)
Multi-Input Action
Perform Action
Action Not Recognized

## Slide 5
Motor Controller Task
Speed Change Flag Raised
Update Encoder
T
F
Check Zero-Value Motor Input
Transferring On
Current Time is Less Than Set Duration
No Data Transferred
Queues Currently Full
T
F
Test Complete = True
Stop Motor and Zero Encoder
Q’s Were Full
T
F
Raise Q’s Were Full
Stop Motor
Put into Time, Position, and Velocity Q’s
T
F
Current Test Complete
New Segment Started
T
F
Decrement New Seg, Start Test Time, Reset Q’s Were Full
T
F
Set Closed Loop Control Reference
Disable Closed Loop Control
T
F
Closed Loop Control Active
Update Gains, Run CLC, Update Reference Value
Test not Completed
F
F
T
T
No Test Running
F

## Slide 6
Data
Transfer Task
Sent Header
Transferring On
Write Header Info To Bluetooth
T
F
(Q’s Empty) and (Test Complete or Q’s Prev Full)
T
F
Q’s Full
T
F
Reset Flags for Next Test
No Data Transferred
Q’s Have Data
T
F
Set
Q’s Prev Full = True
T
Read Q’s
Write to Bluetooth

## Slide 7
Garbage Collector Task
gc.collect()

## Slide 8
Observer Task
Estimate Next Pose Using Gathered Left & Right Motor Voltage, Left & Right Encoder Position, IMU Heading, and IMU Yaw Rate. Store Data in Shares

## Slide 9
Path Director Task
Change Segment
Calibration Segment
Wait For Input Segment
seg = 0
Line Following Segment
Fixed Forward Distance Segment
seg = 1
seg = 3
seg = 2
Line Sensor and IMU Calibrated
F
T / seg = 0
| IMU Heading | ≥ 2π
T / seg = 0
F / seg = 2
Observer Position ≥ 1000mm
T / seg = 0
F / seg = 3

## Slide 10
Task Name
Priority: # Period: # ms Description: …