## Slide 1
User Input
Priority: ∞ Period: 50 ms Description: Monitors for user input to perform actions
Motor Controller
Priority: 2 Period: 20 ms Description: Sets motor speed and updates encoders (will include closed loop motor control)
Data Transfer
Priority: 1 Period: 20 ms Description: Transfers small amounts of data at a time
Garbage Collector
Priority: 0 Period: 0 ms Description: When no other tasks are running collect garbage data for defragmentation
l_flag_s:
[uint8]
r_flag_s:
[uint8]
l_speed_s:
[uint8]
r_speed_s:
[uint8]
l_time_q:
[uint32]
l_pos_q:
[int32]
l_vel_q:
[int32]
r_pos_q:
[int32]
r_vel_q:
[int32]
r_time_q:
[uint32]
data_transfer_s:
[uint8]
test_complete_s:
[uint8]

## Slide 2
User Input Task
Check for Inputs from UART
Pop Cmd from Queue
T
F
Add Input to Cmd Queue
Move Forward
(Both Motors Forward) *
Turn Left
(Right Motor Only)
*
Turn Right
(Left Motor Only)
*
Reverse
(Both Motors Reverse)
*
W
A
S
D
Move Forward
Full Speed
*
Stop Motors, Data Transfer = False, Test Complete = True
G
C
1
2
3
5
Forward 10% Effort
(Both Motors)
*
Forward 20% Effort
(Both Motors)
*
Forward 40% Effort
(Both Motors)
*
Forward 50% Effort
(Both Motors)
*
Forward 30% Effort
(Both Motors)
*
4
6
7
8
0
Forward 60% Effort
(Both Motors)
*
Forward 70% Effort
(Both Motors)
*
Forward 90% Effort
(Both Motors)
*
Forward 100% Effort
(Both Motors)
*
Forward 80% Effort
(Both Motors)
*
9
* Means Data Transfer = True and Test Complete = False
All commands lead to User Input Task

## Slide 3
Motor Controller Task
Speed Change Flag Raised
Update Encoder
T
F
Lower Flag, Set Effort, Start Test Time, Reset Q’s Were Full
Transferring On
Current Time is Less Than Set Duration
T
F
No Data Transferred
Queues Currently Full
T
F
Test Complete = True
Stop Motor and Zero Encoder
Q’s Were Full = False
T
F
Raise Q’s Were Full
Stop Motor
Put into Time, Position, and Velocity Q’s
T
F
Current Test Complete

## Slide 4
Data
Transfer Task
Sent Header
Transferring On
Write Header Info To Bluetooth
T
F
(Q’s Empty) and (Test Complete or Q’s Prev Full)
T
F
Q’s Full
T
F
Reset Flags for Next Test
No Data Transferred
Q’s Have Data
T
F
Set
Q’s Prev Full = True
T
Read Q’s
Write to Bluetooth

## Slide 5
Garbage Collector Task
gc.collect()

## Slide 6
Task Name
Priority: # Period: # ms Description: …